## Slide 1: Network management Communication model
Zeinab MOVAHEDI
Chapter 4 & 5
Network management principles and practices

## Slide 2: Network Management Standards
Notes: Network management standards:
OSI model
Internet model
TMN
IEEE LAN/WAN
Web-based model
Open System Interconnection (OSI) management standard:
Adopted by International Standards Organisation (ISO)
Protocol standard: Common Management Information Protocol (CMIP)
has built-in services => Common Management Information Services (CMIS): specify basic services needed to perform the various functions
Addresses all 7 layers of OSI reference model.
Object-oriented specification
Both LAN/WAN can be managed using CMIP/CMIS
Complex and large CMIP stack (memory of an ordinary workstation not capable to load a complet CMIP stack)
Simple Network Management Protocol (SNMP) standard:
Simple
Industry standard
Primarily intended to manage Internet, but now used to manage WAN and telecommunication systems.
Telecommunication Management Network (TMN):
Manage telecommunication network
Standard of International Telecommunication Union (ITU)
Based on CMIP/CMIS specifications
IEEE:
For WAN and MAN
OSI layer 1 and 2
Both CMIP/CMIS and Internet/SNMP use IEEE for lower layers
Easy to implement => most widely implemented network management system now

## Slide 3: Network management - approches
Notes: Organization
  Network management components
  Functions of components
  Relationships
  Defined in ISO 10040 system management overview
    Specifies object, agent, manager terms
Information
  Structure of management information (SMI)
    Syntax and semantics
  Management information base (MIB)
    Organization of management information
  Object-oriented
Communication
  Mgmt. application processes, layer Mgmt.
  between layers, layer operation within layers
  Transfer syntax with bi-directional messages
  Transfer structure (PDU)
Functions
  User oriented requirements of network management
  Application functions (FCAPS)
    Configure components
    Monitor components
    Measure performance
    Secure information
    Usage accounting
Organization
  Same as OSI model
Information
  Same as OSI, but scalar
Communication
  Messages less complex than OSI and unidirectional
  Transfer structure (PDU)
Functions
  Application functions
    Operations
    Administration
    Security

## Slide 4: Managed LAN
172.17.252.110
172.16.252.1

## Slide 5: Managed hub: system information

## Slide 6: Managed router: system information

## Slide 7: Internet SNMP management
1970 Internet control Message Protocol (ICMP) developped to manage Advanced Research Project Agency Network (ARPANET)
  Packet Internet Groper (PING)
1980 advent of Unix & client-server architecture
  ARPANET developed into the inter-networking
  ARPANET  Internet
1984 Internet Advisory Board (IAB) formed to administor Internet activities
Growth in the Internet, remote monitoring and configuration required
  Simple Gateway Monitoring Protocol (SGMP)
  Simple Network Management Protocol (SNMP)
    Interim solution  de facto standard
      Extensive implementation
      Enormous simplicity
    SNMPv2
    SNMPv3

## Slide 8: SNMP model
Organization Model
  Relationship between network element, agent, and manager
  Hierarchical architecture
Information Model
  Uses ASN.1 syntax
  SMI (Structure of Management Information
  MIB ( Management Information Base)
Communication Model
  Transfer syntax
  SNMP over TCP/IP
  Communication services addressed by messages
  Security framework community-based model

## Slide 9: Two-tier organisation model

## Slide 10: Three-tier organisation model: RMON

## Slide 11: Three-tier organisation model: Proxy server

## Slide 12: SNMP architecture

## Slide 13: System architecture

## Slide 14: SNMP messages
Get-Request
  Sent by manager requesting data from agent
Get-Next-Request
  Sent by manager requesting data on the next MO to the one specified
Set-Request
  Initializes or changes the value of network element
Get-Response
  Agent responds with data for get and set requests from the manager
Trap
  Alarm generated by an agent

## Slide 15: SNMP community

## Slide 16: Community profile

## Slide 17: Generalized administration model

## Slide 18: SNMP protocol specifications
Protocol entities : peer processes implementing SNMP & supporting SNMP application entities
Communication among protocol entities using messages encapsulated in UDP datagrams

## Slide 19: SNMP protocol specifications
SNMP protocol entities received on
  port 162 for traps
  Port 161 for other messages
Maximum length of the protocol on SNMPv1 is 484
The implementtaion of all five PDUs are mandatory
  GetRequest-PDU, GetNextRequest-PDU, GetResponse-PDU, SetRequest-PDU and Trap-PDU
    RFC 1157

## Slide 20: RFC 1157 - SNMP
RFC1157-SNMP DEFINITIONS :: BEGIN
IMPORTS
ObjectName, ObjectSyntax, NetworkAddress, IpAddress, TimeTicks FROM RFC1155-SMI
Message ::= SEQUENCE {
version
INTEGER {
version-1(0)
},
community OCTET STRING,
data ANY
}

## Slide 21: RFC 1157 - SNMP
-- PDUs
GetRequest-PDU ::= [0] IMPLICIT PDU
GetNextRequest-PDU ::= [1] IMPLICIT PDU
GetResponse-PDU ::= [2] IMPLICIT PDU
SetRequest-PDU ::= [3] IMPLICIT PDU

## Slide 22: get & set PDUs
PDU ::= SEQUENCE {
request-id INTEGER,
error-status INTEGER {
      noError(0),
      tooBig(1),
      noSuchName(2),
      badValue(3),
      readOnly(4),
      genErr(5)},
error-index INTEGER,
variable-bindings VarBindList

## Slide 23: Trap PDU

## Slide 24: Trap PDU
Trap-PDU ::= [4] IMPLICIT SEQUENCE {
enterprise OBJECT IDENTIFIER,
agent-addr NetworkAddress,
generic-trap INTEGER {
coldStart(0),
warmStart(1),
linkDown(2),
linkUp(3),
authenticationFailure(4),
egpNeighborLoss(5),
enterpriseSpecific(6)},
    specific-trap INTEGER,
    time-stamp TimeTicks,
    variable-bindings VarBindList
}
VarBind ::= SEQUENCE {
  name ObjectName,
  value ObjectSyntax
}
VarBindList ::= SEQUENCE OF VarBind
END

## Slide 25: Get Request – System group

## Slide 26: IP address table

## Slide 27: Tabular Representation of Aggregate Object

## Slide 28: Object identifier of aggregate objects

## Slide 29: Multiple Instances of Aggregate Managed Object

## Slide 30
MIB for Get-Next-Request
Network Management: Principles and Practice
© Mani Subramanian 2000
5-16
Notes
Chapter 5

## Slide 31
Lexicographic Order
Network Management: Principles and Practice
© Mani Subramanian 2000
5-17
Chapter 5

## Slide 32
MIB Lexicographic Order
A 3.1
B 3.2
T Z
E
1.1
1.2
2.1
2.2
Network Management: Principles and Practice
© Mani Subramanian 2000
5-18
Notes
Chapter 5

## Slide 33
A More Complex MIB Example
Network Management: Principles and Practice
© Mani Subramanian 2000
5-19
Notes
Chapter 5

## Slide 34: Get-Next-Request operation

## Slide 35: Get-Next-Request operation

## Slide 36: SNMP MIB